## Slide 1: Pixhawk and other electronics
A primer
Phil Baldwin
11/8/19

## Slide 2: Electrical Units
Voltage
  Volts (V)
  “Flow” potential
  The only supplied value by a battery
Resistance
  Ohms (Ω)
  Characteristic of a circuit
Current
  Amps (A)
  Resultant of potential and resistance
Power
  Watts (W)
  1 J/s

## Slide 3: Series and Parallel
Ex: AA batteries, nominal 1.5 V, 2000 mAh capacity per cell
  (Just a regular alkaline battery, NOT LiPo)
Series connections increase voltage
  If we put 4 AAs in Series, what is the resulting voltage of the pack? The capacity?
  Voltage: 6V Capacity: 2000 mAh Total Energy: 12 Wh
Parallel connections increase capacity
  If we put 4 AAs in Parallel, what is the resulting voltage of the pack? The capacity?
  Voltage: 1.5V Capacity: 8000 mAh Total Energy: 12 Wh
- 1.5v +
- +
+
-

## Slide 4: LiPo Batteries
Provides an electrical potential → Voltage
Is constructed of cells of a given capacity (mAh)
  Capacity is current * time, hence Amps (or milliamps), over an hour
  Describing a battery by saying “it has 7000 milliamps” is nonsensical, though we can probably guess what you mean
Does not “provide” a set amperage
  Ex: a 20C 4000 mAh LiPo can pump out 80A without damaging the battery, but it will NOT pump out 80A all the time
Most LiPos are sold as a nS1P arrangement, where n is the number of cells in series, and there is just that one set of serial cells (i.e. no parallel arrangement)

## Slide 5: LiPos – Parallel and Series
Generally buy a battery with the series arrangement already done
  Example: You design your propulsion system to use a 4S battery. It is much easier (and probably cheaper) to buy a 4S battery than two 2S batteries and put them in series
Not unheard of to buy two identical batteries and put them in parallel to double the capacity.
  Example: You are planning an extremely long mission which will require approximately 16,000 mAh on a 4S battery. You may not be able to find a single 16,000 mAh 4S battery, but you can source two identical 8,000 mAh 4S batteries.
  Put them in parallel configuration using additional wiring, such as this.
  Be sure to match connector styles, or plan to convert.

## Slide 6: Batteries – Common issues/FAQs
Voltages for LiPos are given as a nominal voltage, 3.7V, which is the voltage at approximately 50% charge
Never discharge a LiPo below 3V/cell
  Example: Absolute minimum on a 4S would be 12.0V
  “We just want to fly another minute” is a bad excuse
“The wires for this battery are huge, but I want to solder on an XT60.”
  You probably purchased a high-discharge rated battery than can handle 120+ amps…there is a good reason the wires are large. Solder on an XT90 and then make or buy a XT90 to XT60 adapter.
“How do we know how much battery we used?”
  Most chargers will read out the mAh charged back into the battery
  Log the mAh consumed within your Pixhawk, the save out the log file

## Slide 7: Pixhawk/PX4/Ardupilot
“Pixhawk” refers to the physical hardware
  Current models
    Pixhawk 2.1 (The Cube)
    Pixhawk 4
    Pixhawk 4 mini
“PX4” and “Ardupilot” refers to the software (firmware) running onboard
  QGroundControl software can install PX4 or Ardupilot
  Mission Planner software can only install Ardupilot
PX4 ≠ Pixhawk 4

## Slide 8: Powering your Pixhawk
Different models have slightly different power connectors, but should come with the correct items to connect to a LiPo battery
  Pixhawk 2 has a “power module” that sits between your LiPo and your ESC
    Comes pre-installed with XT60s
    Also measures battery voltage and current draw
      Nice to monitor for mission duration and battery health
  Pixhawk 4 has options
    A huge, annoying power distribution/IO board that is great for quad- and octo-copters
    In-line power module and compact IO breakout (please buy this)

## Slide 9: Pixhawk – Common issues/FAQs
The connectors are delicate – be nice
Be mindful of board orientation and mounting
Remember that wires take up space
  And have non-zero weight
Purchase 915 MHz radios, not 433 MHz
“The GCS says the battery is too low.”
  Make sure the power module is properly set up in your GCS
“There is no signal to the servos.”
  Make sure the safety switch has been pressed (aka vehicle is “unsafe”)
  Make sure the servos are plugged in to the right location
  Make sure the flight mode is set to your desired mode

## Slide 10: Servos
Defining specification is torque
  Determining your torque requirement is not straightforward
    Depends on aerodynamic loads, hinge axis alignment, manufacturing errors, etc.
LOTS of manufacturers to choose from
Lots of shapes and sizes
  Thin servos might be nice for wings, but probably costs more than a similarly-torque-spec’d “standard” looking model
Make sure their required voltage is being met
  More and more “HV” or High Voltage servos on the market that require more than 6 volts, which is the highest that many ESC-borne BECs will do
  Too low of a voltage can lead to an odd twitch

## Slide 11: Powering your servos
Servos do not get powered by the Pixhawk directly
Voltage must be provided by one of three ways
  Standalone battery pack (4.8V NiMH packs, aka receiver packs can be used)
  BEC that is built-in to your ESC (Most common for this project)
    Note that if your ESC says “opto” or “opto-isolated”, then there is no BEC
  Standalone BEC
    Could be on a separate LiPo as a safety mechanism for running your propulsion battery figuratively into the ground, or be similar to the Pixhawk Power Module (a passthrough)

## Slide 12: Powering your servos, example
Must make sure that current rating of BEC (or battery) is greater than all your servos’ max current draw (with some margin, maybe 25%)
 | Aileron, Elevator Servos | Rudder Servo | Total
Make/Model | Hitec HS-322HD | Hitec HS-125MG | 
Quantity | 3 | 1 | 
Max current (each) | 800 mA | 1200 mA | 
Voltage required | 4.8 – 6.0 | 4.8 – 6.0 | 
Simultaneous max current | 2.4 A | 1.2 A | 3.6 A

## Slide 13: Positive, Negative, and Signal
White/Yellow/Orange: PWM Signal Red: +VDC Black/Brown: -VDC
Servo signal: Pulse Width Modulation
0% deflection: 1100 μs (Note, this can sometimes be reduced to 1000 μs)
50% deflection (“centered”): 1500 μs
100% deflection: 1900 μs (Note, this can sometimes be increased to 2000 μs)
RIGHT |  |  |  | WRONG |  | 

## Slide 14: PWM Signals
Servo signal: Pulse Width Modulation
0% deflection: 1100 μs (Note, this can sometimes be reduced to 1000 μs)
50% deflection (“centered”): 1500 μs
100% deflection: 1900 μs (Note, this can sometimes be increased to 2000 μs)
Throttle signal: Still PWM
Read your ESC’s manual to find the required range (1100-1900 μs? 1000-2000 μs?) of your signal

## Slide 15: Controls Mixing
Can “mix” transmitter controls to do more complex tasks automatically
  Examples
    Deflect elevator up when flaps deployed
    Add right rudder when throttle increased
    Add elevator up when throttle increased (for planes with high-mounted motor)
    Add left/right rudder to counteract adverse yaw in left/right bank
Reduces pilot workload
May be absolutely required in a situation such as a v-tail
Note that when moving to automated flight modes, the mixing will probably be ignored, but compensated for by the autopilot anyhow

## Slide 16: Controls Mixing – RC Transmitter (Tx)
Read each transmitter’s instructions
  Example: Spektrum radios; Enter menu → Mixing → Set mixes 1 – 3
    Flaps mixes (e.g. to deflect elevator) done in the Flaps System menu
    This image shows a transmitter with a 3-position switch used for flaps (normal)
  Make sure deflections are in the correct direction
    Don’t want elevator down when flaps deploy, or else you’re going down REALLY fast
For V-tail
  Glider this fall (no Pixhawk); Set up the Tx with native v-tail mixing (usually in wing/tail setup menu or similar) or use a standalone v-tail mixer.
  With Pixhawk; Do not use Tx v-tail mixing. Re-assign servo outputs for elevator/rudder as left and right v-tails

## Slide 17: Servos – Common issues/FAQs
Make sure your servos are being powered by an appropriate source
  Example of good setup: 5V, 5A BEC powering normal-sized servos
  Example of bad setup: 5V, 2A BEC powering normal sized servos
    Leads to voltage sag, possibly brown-outs
Make sure your servos are centered when installing them
  Example: You take servos straight out of the box, put a servo horn perpendicular to the flat side, and put it in your wing. You power on the servo, and send it a 1500 μs signal. It deflects 45°, and now you must uninstall the servo, move the horn, and reinstall the servo.
“My servo is deflecting the wrong way.” (Looking like flaps instead of ailerons)
  More of an issue when using a servo “Y” cable and a low-channel receiver
  If plugged into its own channel in the Pixhawk, reverse that output
  Some digital servos can be reversed on the servo, but analog servos can not.

## Slide 18: Servos – Common issues/FAQs
“My servo isn’t moving at all.”
  90% of the time a servo wire is hooked up incorrectly
  Check your GCS servo output page to see if a signal is being sent
  Make sure the servo is powered (battery, BEC, etc) powering the servo rail
“The servo is all jittery.”
  Servo rail voltage may be too high/low
  Sometimes servos have a tiny bit of jitter because of their dead band circuitry
    Usually goes away under load
“Why is the servo getting so hot?”
  May be overloaded (more torque than the servo can handle)
  Servo rail voltage may be too high/low

## Slide 19: Suggestions
Read your product manuals
  Or at least skim the important parts
  Valuable tidbits like “How to hook everything up”
Set up an “iron bird”
  Basic testbed for your electronics, mounted to one piece of material so you can carry it around
  Can include Pixhawk, servos, batteries, GPS, etc.
  Can make it in 5 minutes out of foamboard and tape – it need not be pretty
Try to have access to a digital multimeter
  Best basic electrical troubleshooting tool
    Voltage testing
    Continuity testing

## Slide 20: Suggestions
List out all electrical connections before you purchase components
  Figure out if you need to replace a battery, ESC connector, etc.
  Figure out if you need to buy different size bullet connectors for your motor/ESC
Build an electrical budget (for power draw, not $$)
  Investigate whether any additional systems will require separate power sources due to voltage differences or system architecture reasons
Produce a nice (high quality) and easy-to-follow electrical diagram
  Include cable and connector types, peripherals, what power is going where, etc.
  Does not need to be analogous to the aircraft layout, but it can be

## Slide 21: Example
Not perfect
It is CLEAR
It includes all components
  Except connectors…
It breaks down the complex system
  Pixhawk wiring separate from payload system
  Shows the interconnectivity between the two
Wrong