## Slide 1: Propellers
Phil Baldwin
10/11/2019

## Slide 2
For a constant pitch propeller
(most model airplane propellers)
Propeller Geometry
Pitch is defined as "the distance a propeller would move in one revolution if it were moving through a soft solid, like a screw through wood." For example, a 12-pitch propeller would move forward 12 inches in one revolution. Pitch ratio is usually a generalized comparator used to define groups of propeller type and operation. Generally, higher pitch ratio means higher operating speed.

## Slide 3: Propeller Parameters
 freestream density
n propeller revolutions per second
D propeller diameter [L units]
V freestream velocity [L /second units]
Power coefficient Thrust coefficient Advance ratio
Efficiency

## Slide 4
Chart: J - Advance Ratio
| 0.02 | 0.05 | 7.0000000000000007E-2 | 0.1 | 0.12 | 0.14000000000000001 | 0.17 | 0.19 | 0.22 | 0.24 | 0.26 | 0.28999999999999998 | 0.31 | 0.33 | 0.36 | 0.38 | 0.41 | 0.43 | 0.45 | 0.48 | 0.5 | 0.53 | 0.55000000000000004 | 0.56999999999999995 | 0.6 | 0.62 | 0.65 | 0.67 | 0.69
Thrust Coefficient | 0.0834 | 0.077 | 0.0704 | 0.0646 | 0.0589 | 0.0535 | 0.0508 | 0.049 | 0.047 | 0.0451 | 0.0431 | 0.0411 | 0.0391 | 0.037 | 0.0349 | 0.0327 | 0.0305 | 0.0282 | 0.0259 | 0.0235 | 0.0211 | 0.0186 | 0.0161 | 0.0136 | 0.011 | 0.0083 | 0.0056 | 0.0028 | 0
Power Coefficient | 0.0448 | 0.0416 | 0.0386 | 0.0356 | 0.0327 | 0.03 | 0.0288 | 0.028 | 0.0273 | 0.0265 | 0.0257 | 0.0249 | 0.024 | 0.0231 | 0.0221 | 0.0211 | 0.02 | 0.0189 | 0.0177 | 0.0165 | 0.0152 | 0.0139 | 0.0126 | 0.0112 | 0.0097 | 0.0081 | 0.0066 | 0.005 | 0.0035
Efficiency | 0.0445 | 0.0884 | 0.1309 | 0.1734 | 0.2151 | 0.2559 | 0.2956 | 0.3341 | 0.3713 | 0.4071 | 0.4416 | 0.4747 | 0.5065 | 0.537 | 0.5659 | 0.5934 | 0.6191 | 0.6428 | 0.6641 | 0.6818 | 0.6957 | 0.7032 | 0.7041 | 0.6962 | 0.6758 | 0.6323 | 0.5466 | 0.374 | -0.0039
APC 12 x 6 E Propeller

## Slide 5
Chart: APC 12 x 6 E Propeller 15000 RPM
| 0 | 4.0999999999999996 | 8.1 | 12.2 | 16.3 | 20.399999999999999 | 24.4 | 28.5 | 32.6 | 36.700000000000003 | 40.700000000000003 | 44.8 | 48.9 | 53 | 57 | 61.1 | 65.2 | 69.3 | 73.3 | 77.400000000000006 | 81.5 | 85.6 | 89.6 | 93.7 | 97.8 | 101.8 | 105.9 | 110 | 114.1 | 118.1
 | 12.399 | 11.441 | 10.462 | 9.596 | 8.756 | 7.944 | 7.555 | 7.276 | 6.992 | 6.703 | 6.412 | 6.115 | 5.811 | 5.501 | 5.185 | 4.861 | 4.53 | 4.192 | 3.847 | 3.495 | 3.135 | 2.769 | 2.396 | 2.016 | 1.628 | 1.232 | 0.829 | 0.417 | -0.003
APC 12 x 6 E Propeller

## Slide 6: Propeller analysis
Gold.m
  Gold Propeller Notes
JavaProp
Approximate Model
  For conceptual and motor/propeller matching
Experimental and Calculation Data Bases
MotoCalc
http://www.mh-aerotools.de/airfoils/

## Slide 7: Approximate Model
Thrust Coefficient
  point where thrust is zero
  is an empirical factor based on propeller data
Power Coefficient
The solidity where B=# of blades, c= chord and R=radius
McCormick “Aerodynamics, Aeronautics and Flight Mechanics” Equation 6.54 with g=1
Efficiency

## Slide 8: Comparison of Gold to Approximate Method
Increasing
Pitch
Increasing
Pitch
Increasing
Pitch

## Slide 9
Comparison of UIUC Data to Approximate Method
Chart: APC 19x12E
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.14000000000000001 | 0.17 | 0.2 | 0.23 | 0.26 | 0.28999999999999998 | 0.32 | 0.35 | 0.37 | 0.4 | 0.43 | 0.46 | 0.49 | 0.52 | 0.55000000000000004 | 0.57999999999999996 | 0.61 | 0.63 | 0.66 | 0.69 | 0.72 | 0.75 | 0.78 | 0.81 | 0.84
Ct approx | 0.15 | 0.144 | 0.138 | 0.132 | 0.126 | 0.122 | 0.116 | 0.11 | 0.104 | 0.098 | 0.092 | 0.086 | 0.08 | 0.076 | 0.07 | 0.064 | 0.058 | 0.052 | 0.046 | 0.04 | 0.034 | 0.028 | 0.024 | 0.018 | 0.012 | 0.006 | 0 | -0.006 | -0.012 | -0.018
Cp approx | 0.028909 | 0.031285 | 0.033437 | 0.035361 | 0.037055 | 0.038054 | 0.039355 | 0.040415 | 0.041228 | 0.04179 | 0.042094 | 0.042135 | 0.041906 | 0.041601 | 0.04091 | 0.039933 | 0.038665 | 0.037099 | 0.035231 | 0.033055 | 0.030566 | 0.027761 | 0.025712 | 0.02237 | 0.0187 | 0.0147 | 0.010368 | 0.0056996 | 0.00069353 | -0.0046524
sleig Ct | 0.0659 | 0.0619 | 0.0565 | 0.0521 | 0.0456 | 0.0418 | 0.0345 | 0.03 | 0.0235 | 0.0192 | 0.013 | 0.0081 | 0.0022 | -0.0033 | 0.0884 | 0.0864 | 0.0841 | 0.0813 | 0.0783 | 0.0752 | 0.0719 | 0.0671 | 0.0627 | 0.0578 | 0.0525 | 0.0422 | 0.0368 | 0.0292 | 0.0246
selig Cp | 0.0416 | 0.0408 | 0.0393 | 0.0379 | 0.0353 | 0.0337 | 0.0302 | 0.028 | 0.0249 | 0.0227 | 0.0193 | 0.0167 | 0.0134 | 0.0102 | 0.0412 | 0.0414 | 0.0419 | 0.042 | 0.042 | 0.0419 | 0.0418 | 0.0411 | 0.0403 | 0.039 | 0.0373 | 0.0331 | 0.0307 | 0.0267 | 0.0245
Approx Eff | 0 | 0.13809 | 0.24763 | 0.33596 | 0.40804 | 0.44883 | 0.50108 | 0.54435 | 0.58018 | 0.60972 | 0.63382 | 0.65314 | 0.66816 | 0.67594 | 0.68443 | 0.68915 | 0.69003 | 0.68681 | 0.67895 | 0.66556 | 0.64516 | 0.61526 | 0.58805 | 0.53108 | 0.44278 | 0.29387 | 0
selig Eff | 0.677 | 0.688 | 0.696 | 0.699 | 0.693 | 0.687 | 0.665 | 0.645 | 0.597 | 0.554 | 0.459 | 0.344 | 0.121 | -0.244 | 0.398 | 0.439 | 0.492 | 0.534 | 0.57 | 0.601 | 0.628 | 0.653 | 0.667 | 0.676 | 0.678 | 0.665 | 0.655 | 0.629 | 0.604
http://www.apcprop.com/v/downloads/PERFILES_WEB/datalist.asp
http://aerospace.illinois.edu/m-selig/props/propDB.html

## Slide 10
Comparison of UIUC Data to Approximate Method
Chart: APC 9x 6 E
| 0 | 0.03 | 0.06 | 0.09 | 0.12 | 0.15 | 0.18 | 0.21 | 0.24 | 0.27 | 0.3 | 0.33 | 0.36 | 0.39 | 0.42 | 0.45 | 0.48 | 0.51 | 0.54 | 0.56999999999999995 | 0.61 | 0.64 | 0.67 | 0.7 | 0.73 | 0.76 | 0.79 | 0.82 | 0.85 | 0.88
Ct approx | 0.168 | 0.1608 | 0.1536 | 0.1464 | 0.1392 | 0.132 | 0.1248 | 0.1176 | 0.1104 | 0.1032 | 0.096 | 0.0888 | 0.0816 | 0.0744 | 0.0672 | 0.06 | 0.0528 | 0.0456 | 0.0384 | 0.0312 | 0.0216 | 0.0144 | 0.0072 | 0 | -0.0072 | -0.0144 | -0.0216 | -0.0288 | -0.036 | -0.0432
Cp approx | 0.030377 | 0.034616 | 0.038463 | 0.041917 | 0.044978 | 0.047645 | 0.049916 | 0.05179 | 0.053266 | 0.054343 | 0.055019 | 0.055291 | 0.05516 | 0.054622 | 0.053676 | 0.052321 | 0.050554 | 0.048374 | 0.04578 | 0.042769 | 0.038106 | 0.034119 | 0.029711 | 0.024883 | 0.019631 | 0.013956 | 0.007857 | 0.0013328 | -0.0056171 | -0.012993
selig | 0.1091 | 0.1071 | 0.1057 | 0.1034 | 0.1012 | 0.0985 | 0.0963 | 0.0938 | 0.0896 | 0.0877 | 0.0844 | 0.0807 | 0.077 | 0.0729 | 0.067 | 0.0608 | 0.0526 | 0.0572 | 0.0497 | 0.0434 | 0.0372 | 0.0303 | 0.0252 | 0.0191 | 0.0141 | 0.0065 | 0.0026 | -0.0059 | -0.0104 | -0.0171 | -0.0229 | -0.0293
selig cp | 0.0527 | 0.0531 | 0.0535 | 0.0536 | 0.0538 | 0.054 | 0.0541 | 0.0539 | 0.0535 | 0.0539 | 0.0539 | 0.0536 | 0.0535 | 0.0528 | 0.0511 | 0.0489 | 0.0459 | 0.0472 | 0.0442 | 0.0416 | 0.039 | 0.036 | 0.0337 | 0.031 | 0.0289 | 0.0255 | 0.0238 | 0.0196 | 0.0173 | 0.0138 | 0.0105 | 0.0069
APC Ct | 0.1094 | 0.1036 | 0.0958 | 0.0906 | 0.0854 | 0.0803 | 0.0753 | 0.0722 | 0.0694 | 0.0666 | 0.0637 | 0.0607 | 0.0578 | 0.0547 | 0.0516 | 0.0484 | 0.0452 | 0.0418 | 0.0384 | 0.0349 | 0.0314 | 0.0277 | 0.024 | 0.0202 | 0.0163 | 0.0123 | 0.0083 | 0.0042 | 0
Approx Eff | 0 | 0.13936 | 0.23961 | 0.31433 | 0.37138 | 0.41557 | 0.45004 | 0.47685 | 0.49742 | 0.51274 | 0.52346 | 0.52999 | 0.53256 | 0.53122 | 0.52582 | 0.51605 | 0.50133 | 0.48075 | 0.45295 | 0.41581 | 0.34578 | 0.27012 | 0.16236 | 0
selig Eff | 0.197 | 0.247 | 0.289 | 0.326 | 0.361 | 0.398 | 0.43 | 0.459 | 0.481 | 0.506 | 0.524 | 0.54 | 0.55 | 0.559 | 0.563 | 0.559 | 0.548 | 0.548 | 0.538 | 0.525 | 0.506 | 0.472 | 0.436 | 0.377 | 0.311 | 0.171 | 0.075 | -0.221 | -0.447 | -0.959 | -1.746 | -3.517
http://www.apcprop.com/v/downloads/PERFILES_WEB/datalist.asp
http://aerospace.illinois.edu/m-selig/props/propDB.html

## Slide 11: Sources of Propeller Data and Calculations
UIUC Propeller Data Base
  https://m-selig.ae.illinois.edu/props/propDB.html
APC Propellers (https://www.apcprop.com/)
  Calculation Data base
  https://www.apcprop.com/technical-information/performance-data/

## Slide 12: Some thoughts on practical application
APC Props has suggested RPM limits based on the type of propeller
  In general, none of the projects in AerosPACE will be using a SF (slow flyer) propeller – they are light and thin, and have great data! But they could rip themselves apart if above the safe RPM.
  Thin Electric (have an E in the prop name) are most widely used
  Pusher props (nominal LH rotation instead of RH) are available as well
There are RC-sized props that are made with 3+ blades
  Generally used for a “scale aircraft” look
  Using a 3-bladed propeller to achieve the same thrust as a 2-bladed propeller of the same diameter will always be less efficient
  Limited selection
Balance your propellers before you spin them up – vibrations destroy airframes
There must be a balance struck between takeoff and cruise performance